## Slide 1: Otazky
Kódy a čísla

## Slide 2
l. 2 x 101 + 8 x 10° is equal to
(a) IO (b) 280 (c) 2.8 (d) 28
2. The binary number 1101 is equal to the decimal number
(a) 13 (b) 49 (c) 11 (d) 3
3. The binary number 11011101 is equal to the decimal number
(a) 121 (b) 22 1 (c) 441 (d) 256
4. The decimal number 17 is equal to the binary number
(a) 10010 (b) 11000 (c) 10001 (d) 01001
5. The decimal number 175 is equal to the binary number
(a) 11001111 (b) 10101110 (c) 10101111 (d) 11101111
6. The sum of 11010 + 01111 equals (a) 101001 (b) 101010 (c) 110101 (d) 101000
7. The difference of 110 - 010 equals
(a) 001 (b) 010 (c) 101 (d) 100

## Slide 3
8. The 1's complement of 10111001 is
(a) 01000111 (b) 01000110 (c) 11000110 (d) 10101010
9. The 2's complement of 11001000 is
(a) 00110111 (b) 00110001 (c) 01001000 (d) 10101010
9. The decima1 number +122 is expressed in the 2's complement form as
(a) 00110111 (b) 11111010 (c) 01000101 (d) 10000101
l0. The decimal number -34 is expressed in the 2's complement form as (a)
01011110 (b) 10100010 (c)11011110 (d) 01011101
11. A single-precision floating-point binary number has a total of
  8 bits (b) 16 bits (c) 24 bits (d) 32 bits
12. In the 2's comp1ement form, the binary number 10010011 is equal to the decimal number
(a) -19 (b) + 109 (c) +9 1 (d) - 109

## Slide 4
13. In the 2's comp1ement form, the binary number 10010011 is equal to the decimal number
-19 (b) + 109 (c) +91 (d) – 109
14. The binary number 101100111001010100001 can be written in octal as
(a)54712308 (b) 54712418 (c) 26345218 (d) 231625018
15. The binary number 10001101010001101111 can be written in hexadecimal as
(a) AD46716 (b) 8C46F16 (c) 8D46F16 d) AE46F16
16. The binary number for F7A916 is
1111011110101001 (c) 1111111010110001
1110111110101001 (d) 1111011010101001
17. The BCD number for decimal 473 is
111011010 (b) 110001110011 (c) 010001110011 (d) 010011110011

## Slide 5
1. What is the weight of the digit 6 in each of the following decimal numbers ?
(a) 1386 (b) 54,692 (c) 671,920
2. Express each of the following decimal numbers as a power of ten:
(a) 10 (b) 100 (c) 10,000 (d) 1,000,000
3. Give the value of each digit in the following decimal numbers:
(a) 471 (b) 9356 (c) 125,000
4. How high can you count with four decimal digits ?
5. Convert the following binary numbers to decimal:
a)11 b)100 (c) 111 (d)1000 (e) 1001 (f) 1100 (g) 1011 (h) 1111
6. Convert the following binary numbers to decima1:
(a) 1110 (b) 1010 (c) 11100 (d) 10000
(e) 10101 (f) 11101 (g) 10111 (h)11111

## Slide 6
7. Convert each binary number to decimal:
(a) 110011.11 (b) 101010.01 (c) 1000001.111 (d) 1111000.101
(e) 1011100.10101 (f) 1110001.0001 (g) 1011010. 1010
(h) 1111111.11111
8.What is the highest decimal number that can be represented by each of the following numbers of binary digits (hits)?
9.How many bits are required to represent the following decimal numbers ?
17 (b) 35 (c) 49 (d) 68 (e) 81 (f) 114 (g) 132 (h) 205
10. Generate the binary sequence for each decimal sequence:
0 through 7 (b) 8 through 15 (c) 16 through 31
(d) 32 through 63 (e) 64 through 75

## Slide 7
11. Convert each decimal number to binary by using the sum-of-weights method:
(a) 10 (b) 17 (c) 24 (d) 48
(e) 61 (f) 93 (g) 125 (h) 186
12. Convert each decimal fraction to binary using the sum-of-weig hts method:
(a) 0.32 (b) 0.246 (c) 0.0981
13. Convert each decimal number to binary using repeated division by 2:
(a)15 (e) 40 (b)21 (f) 59 (c) 28 (g) 65 (d) 34 (h) 73
14. Convert each decimal fraction to binary using repeated multiplication by 2:
(a) 0.98 (b) 0.347 (c) 0.9028

## Slide 8
21. Express each decimal number in binary as an 8-bit sign-magnitude number:
(a) + 29 (b) -85 (c) +100 (d) -123
22. Express each decimal number as an 8-bit number in the l's complement form:
(a) -34 (b) + 57 (c) -99 (d) + 115
23. Express each decimal number as an 8-bit number in the 2's comp1ement form:
(a) +12 (b) -68 (c) +101 (d) -125
24. Determine the decimal value of each signed binary number in the sign-magnitude form:
(a) 10011001 (b) 01110100 (c) 10111111

## Slide 9
35. Convert each hexadecimal number to binary:
(a) 3816 (b) 5916 (c) A14 16 (d) 8D16 (e) 4100 16 (f) FB17 16 (g) 8A9D16
36. Convert each binary number to hexadecimal:
1110 (b) 10 (c) 10111 (d) 10100110 (e) 1111110000 (f) 100110000010
37. Convert each hexadecimal number to decimal:
(a) 23 16 (c) 1A16 (d) 8D 16 (e) F316 (g) 5C2 16 (h) 70016
38. Convert each decimal number to hexadecimal:
(a) 8 (b) 14 (c) 33 (d) 52 (e) 284 (f) 2890 (g) 4019 (h) 6500
39. Perform the following additions:
(a) 37 16 + 29 16 (b) A016 + 6B16 (c) FF16 + BB 16
40. Perform the following subtractions:
(a) 516- 4016 (b) C8 16- 3A16 (c) FD 16 - 8816

## Slide 10: logika

## Slide 22: Booleova algebra